## Slide 1: ECE 721 Trace Caches
  Spring 2021
  Prof. Eric Rotenberg

## Slide 2: High ILP Processors
High ILP processor
  Many parallel execution lanes
    Between 4 and 16
  Large window to find enough independent instructions to keep execution lanes busy
    Large PRF, IQ, LQ/SQ
Implications for instruction fetch?
  Fetch rate must match execution rate
  If 16 execution lanes, ideally need a sustained fetch rate of 16 instr./cycle

## Slide 3: Instruction Fetch Issues
Branch throughput
  Predict more than one branch per cycle
Noncontiguous instruction blocks
  Fetch past taken branches
Instruction Cache
not taken
taken
A
B
C

## Slide 4: Noncontiguous Instructions
Fundamental problem
  Conventional I$ stores instructions in their static order
  Decoder wants to see instructions in their dynamic order
Two classes of hardware solutions
  Deal with conventional instruction cache: Construct dynamic order on-the-fly
  Direct approach: Cache instructions in dynamic order

## Slide 5: Trace Cache Concept
A
t
t
trace: {A, taken, taken}
Trace Cache
Fill new trace from instruction cache
A
t
t
trace: {A, taken, taken}
Trace Cache
Access existing trace
using A and predictions (t, t)
later...
{ A, t , t }
to DECODER

## Slide 6
A
A
A
A
A
MUX
A
multiple
branch
predictor
path
match?
A
instruction cache
trace cache
instruction cache
trace cache

## Slide 7: Trace Selection
Trace selection
  Constraints for forming traces
  Hardware-determined constraints
  Goal-oriented constraints

## Slide 8: Trace Selection (cont.)
Hardware-determined constraints
  Maximum of n instructions (trace cache line size)
  Maximum of m conditional branches (predictor bandwidth = m predictions/cycle)
  End trace at certain branch types (more later)

## Slide 9: Trace Selection (cont.)
Goal-oriented constraints
  Maximize number of instructions delivered if T$ hit
    Make n and m large for long traces
  Minimize T$ miss rate
    n and m too large => number of unique traces explodes
    Too many unique traces can’t all be stored in T$

## Slide 10: Trace Selection (cont.)
721sim trace selection (modified from MICRO-29 paper)
  Maximum of “n” instructions (for example, 16 instructions)
    Constrained by trace cache’s line size
  Maximum of “m” conditional branches (for example, 3 cond. branches)
    Constrained by how many branch predictions can be supplied each cycle by the multiple-branch predictor
  Trace may contain any number of direct jumps
    Jump-direct doesn’t consume a cond. branch prediction, and target is fixed
  End trace (but do not discard it, unlike MICRO-29) at the following branch types:
    Call direct
      Why: To simplify RAS management. Only one RAS push per cycle.
    Jump indirect
      Jump-indirect has a dynamic (varying) target
      If it were embedded, trace hit logic would have to compare its embedded target against the indirect-predictor’s predicted target
      Not embedding jump-indirect reduces number of unique traces => lower miss rate
    Call indirect, return
      Why: (1) Simplify RAS management. Only one push/pop per cycle. (2) Same reasons as jump-indirect.
    System calls

## Slide 11: Trace Cache Contents (modified from MICRO-29)
n instructions
Control information
  Tag: Upper bits of start PC of trace
  Branch flags: m-1 conditional branch directions
  Branch mask: Encodes the number of embedded conditional branches
  ends_in_branch flag: true if trace ends in a branch
  end_branch_type: if ends_in_branch, the type guides where to get the next PC from (either from T$ or from core fetch unit)
  Trace fall-through address:
    Next PC if trace doesn’t end in a branch, or if trace ends in a conditional branch and it is predicted not-taken.
    This field is also used by call-direct and call-indirect to hold their PC+1, which is to be pushed onto the RAS.
  Trace target address: Next PC if trace ends in a conditional branch and it is predicted taken, or if trace ends in a jump-direct or call-direct.

## Slide 12: Trace Cache Detail
BTB
RAS
interchange & shift
CORE FETCH UNIT
FETCH
ADDRESS
A 01 11 1 cb X Y
fill unit
hit logic
PRED
MUX
to DECODER
tag
branch
flags
branch
mask
target
address
fall-thru
address
m (3)
predictions
n (16)
instructions
n (16)
instructions
TRACE CACHE
INSTR. CACHE
ends_in_branch
end_branch_type

## Slide 13: Breakdown of Fetch Address
Assuming 32-bit addresses and 4 bytes/instr.
T$ tag
T$ index
00
log2(# trace cache sets)
low two bits always 0
32 - (# index bits) - 2

## Slide 14: Example
EX:
  64KB 4-way set-associative T$
  Trace size = 16 4-byte instructions
# sets = 64KB / (4 traces/set * 16 instr./trace * 4 bytes/instr.)
= 256
# index bits = log2(# sets) = 8
T$ tag
T$ index
00
2
8
22

## Slide 15: Branch Mask (implementation modified w.r.t. MICRO-29)
Encodes the number of embedded conditional branches
  Number of embedded conditional branches = number of leading 1’s in the mask
If m = 3 (up to 3 conditional branches):
# embedded cond. br.
2
1
0
3 (not possible)
branch_mask
11
10
00

## Slide 16: Examples (n=16, m=3)
example trace |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | branch_mask | ends_in_branch flag
 |  | b |  |  |  |  | b |  |  |  | b |  |  |  |  | 11 | 1
 |  | b |  |  |  |  | b |  |  |  |  |  |  |  | b | 11 | 1
 |  | b |  |  |  |  | b |  |  |  |  |  |  |  |  | 11 | 0
 |  | b |  |  |  |  |  |  |  |  |  |  |  |  | b | 10 | 1
 |  | b |  |  |  |  |  |  |  |  |  |  |  |  |  | 10 | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | b | 00 | 1
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 00 | 0

## Slide 17: T$ Hit Logic
Use index to read out trace(s)
Hit conditions
  1. Start PC check:
  Tag from fetch address ==
  Tag from trace cache
  2. Path check:
  (branch_mask & predictions) ==
  (branch_mask & branch_flags)

## Slide 18: Next-PC logic without Trace Cache
next PC | conditions
misp. recovery PC from Execute | Execute stage signals mispredicted branch
BTB-miss recovery PC from Decode | Decode stage signals misfetched bundle due to BTB misses in prior cycle
PC + fetch_width | I$ fetch bundle doesn’t end in a predicted-taken cond. br. or unconditional br.
target from banked BTB | I$ fetch bundle ends in a predicted-taken cond. br. or jump/call direct
target from dedicated indirect-branch predictor | I$ fetch bundle ends in jump/call indirect
target from RAS | I$ fetch bundle ends in return

## Slide 19: Next-PC logic with Trace Cache
next PC | conditions
misp. recovery PC from Execute | Execute stage signals mispredicted branch
BTB-miss recovery PC from Decode | Decode stage signals misfetched bundle due to BTB misses in prior cycle (only possible if bundle came from I$, not T$)
PC + fetch_width | T$ miss && I$ fetch bundle doesn’t end in a predicted-taken cond. br. or unconditional br.
target from banked BTB | T$ miss && I$ fetch bundle ends in a predicted-taken cond. br. or jump/call direct
target from dedicated indirect-branch predictor | (T$ miss && I$ fetch bundle ends in jump/call indirect) ¦¦ (T$ hit && ends_in_branch && (end_branch_type == jump/call indirect))
target from RAS | (T$ miss && I$ fetch bundle ends in return) ¦¦ (T$ hit && ends_in_branch && (end_branch_type == return))
trace fall-through address | T$ hit && (!ends_in_branch ¦¦ ((end_branch_type == cond. br.) && (its prediction is not-taken)))
trace target address | T$ hit && ends_in_branch && ((end_branch_type == jump/call direct) ¦¦ ((end_branch_type == cond. br.) && (its prediction is taken)))

## Slide 20: RAS management
action | condition | PC to push on RAS
push RAS | I$ fetch bundle ends in call direct/call indirect | PC + fetch_bundle_length (same as call’s PC+1)
pop RAS | I$ fetch bundle ends in return | n/a
action | condition | PC to push on RAS
push RAS | ends_in_branch && (end_branch_type == call direct/call indirect) | trace fall-through address (same as call’s PC+1)
pop RAS | ends_in_branch && (end_branch_type == return) | n/a
If no trace cache or T$ miss:
If T$ hit:

## Slide 21: T$ Redundancy & Fragmentation
A
A
B
C
D
CFG
Instruction Cache
A
C
A
B
D
B
D
C
D
Trace Cache
fragmentation
redun-
dancy

## Slide 22: Design Space
Conventional
  Size
  Set-associativity
Specific to trace cache
  Partial matching
  Path-associativity
  Indexing methods (including predictions)
  Trace selection policies
  Trace cache fill options

## Slide 23: Partial Matching
Return part of trace if only prefix matches
Must add fall-through & target addresses for each embedded branch (not just trace-ending branch)
  Needed for next-PC logic

## Slide 24: Path-Associativity
Definition
  Ability to store different traces with same start PC
Set-associative trace cache
  Normal associativity gives path-associativity
Direct-mapped trace cache
  Combine PC with prediction bits to form trace cache index (e.g., concatenate, XOR, etc.)
  Different traces with same start PC will map to different sets

## Slide 25: Indexing Methods
Include prediction bits in trace cache index for path-associativity
  How many bits?
  XOR or concatenate? XOR with which PC bits?
Modifying indexing does not change hit logic

## Slide 26: Trace Cache Fill Options
When to build traces and update T$
  Fetch stage
  Retire stage
Build one or multiple traces at a time
        OR
Trace A
Trace B
Trace C
Trace A’
Trace B’
Trace C’
Trace A
Trace B
Trace C
etc...
Same dynamic
instruction stream,
multiple starting
points

## Slide 27: Other Trace Cache Applications
Use in new microarchitectures
  Trace processors
Trace pre-processing
  Either improves performance, reduces pipeline complexity, or both
  Examples
    Compiler-like optimizations (dead code removal, constant propagation, strength reduction, etc.)
    Re-schedule instructions (allows simple issue logic, e.g., in-order, without degrading performance)
    Pre-renaming (simplify renaming logic)